## Slide 1: Handheld 3D Printed Fan
MANUFACTURING TECHNOLOGY · PROJECT
Design, additive manufacturing and safety analysis of a portable cooling device
Team: [Member names] · Guide: [Faculty name]
[Department, Institute] · [Date]
Notes: Introduce the project in one sentence: we designed, 3D printed, assembled and tested a handheld fan, and analysed its safety. Mention team members and guide before moving on.

## Slide 2: What we set out to do
01 · TITLE & OBJECTIVES
PROJECT TITLE
Design and Fabrication of a Handheld 3D Printed Fan
Manufacturing Technology project
01
Design a compact, ergonomic handheld fan in CAD.
02
Select a suitable filament and tune the FDM print settings.
03
Fabricate, assemble and test a working prototype.
04
Identify hazards and apply safety devices and standards.
05
Evaluate cost, performance and scope for improvement.
Handheld 3D Printed Fan · Manufacturing Technology
02
Notes: State the project title, then walk through the five objectives. These objectives map to the slides that follow: design, material and process, fabrication and testing, safety, and evaluation.

## Slide 3: Contents
OVERVIEW
01
Title and objectives
02
Background
03
Problem and case description
04
Design and manufacturing
05
Hazard analysis
06
Safety devices and standards
07
Human factors
08
Preventive measures
09
Testing, conclusion and references
Handheld 3D Printed Fan · Manufacturing Technology
03
Notes: Quick roadmap. The structure follows the department’s PPT guidelines, applied to a manufacturing project: design and process first, then hazards, safety devices, human factors and preventive measures.

## Slide 4: Why additive manufacturing?
02 · BACKGROUND
Layer by layer
Parts are built from a digital model, so complex shapes need little tooling.
Personal cooling
Handheld fans give low-cost relief where air conditioning or mains power is not available.
Fast iteration
A design change needs a new CAD file and a reprint, not a new mould.
Project focus: FDM (fused deposition modelling) with [PLA / PETG] filament on a desktop printer [printer model].
Handheld 3D Printed Fan · Manufacturing Technology
04
Notes: Explain additive manufacturing briefly: the model is sliced into layers and built up. Then connect it to the fan: low cost, quick design changes, and no tooling. Fill in the filament and printer you actually used in the teal box.

## Slide 5: Problem statement
03 · PROBLEM / CASE DESCRIPTION
Low-cost handheld fans come in one fixed design and are hard to customise or repair. Can we make a light, safe and comfortable one on a 3D printer?
Part fit
Printed blades and housing must balance well and fit the motor shaft.
Safety
Spinning blades and a lithium cell must be guarded and protected.
Usability
Weight, grip and noise decide whether the fan is comfortable to hold.
Handheld 3D Printed Fan · Manufacturing Technology
05
Notes: Read the problem statement aloud. Then name the three challenges that drive the rest of the project: fit and balance, safety, and comfort in the hand.

## Slide 6: Specifications we designed to
04 · DESIGN REQUIREMENTS
Parameter | Target | Reason
Overall size | Fits one hand, [__] mm | Easy to carry
Weight | Under [__] g | No fatigue when held
Blade diameter | [__] mm | Fits inside the guard
Power source | [3.7 V Li-ion cell] | Rechargeable, portable
Motor | [DC motor, __ RPM] | Matched to blade size
Run time | [__] h per charge | Practical daily use
Print material | [PLA / PETG] | Low cost, easy to print
Handheld 3D Printed Fan · Manufacturing Technology
06
Notes: Replace every bracketed value with your actual numbers before presenting. Explain how each requirement links to the problem statement, especially weight and size for comfort.

## Slide 7: CAD model and parts
04 · DESIGN & COMPONENTS
Part | Function | Source
Blade set | Moves the air | Printed
Guard grill | Keeps fingers out | Printed
Motor housing | Holds motor and switch | Printed
Handle | Grip and battery bay | Printed
Motor, cell, switch | Drive and power | Bought
Handheld 3D Printed Fan · Manufacturing Technology
07
Notes: The drawing is a simple schematic. Replace it with a screenshot of your CAD model if you have one. Walk through the four printed parts and the three bought components.

## Slide 8: Choosing the filament
04 · MATERIAL SELECTION
Property | PLA | PETG | ABS
Ease of printing | Easy | Moderate | Hard, warps
Toughness | Brittle | Tough | Tough
Softening point | About 60 °C | About 80 °C | About 105 °C
Fumes | Low odour | Low odour | Needs ventilation
Fit for this fan | Good for prototypes | Best for durability | Not preferred
Selected: [PLA / PETG], because [your reason]. Update this to match your build.
Handheld 3D Printed Fan · Manufacturing Technology
08
Notes: The softening temperatures are approximate and vary by brand, so quote your filament datasheet if you have one. A hand-held fan sits in a warm environment, so heat resistance and toughness matter as much as ease of printing.

## Slide 9: From CAD to finished fan
04 · MANUFACTURING PROCESS
01
CAD modelling
Parts modelled and checked for fit.
02
STL export
Mesh checked and oriented for printing.
03
Slicing
Layer height, infill and supports set.
04
FDM printing
Parts printed in the chosen filament.
05
Finishing
Supports removed, edges sanded, blades balanced.
06
Assembly and test
Motor, cell and switch fitted, then tested.
Handheld 3D Printed Fan · Manufacturing Technology
09
Notes: Walk the six steps in order. If you iterated, say how many reprints it took and what you changed, for example blade pitch or the motor mount tolerance.

## Slide 10: Slicer settings used
04 · PRINTING PARAMETERS
Parameter | Setting | Why
Printer | FDM, 0.4 mm nozzle | Common and low cost
Layer height | 0.2 mm | Balance of speed and finish
Infill | 20 to 30 % | Light yet stiff
Walls | 3 perimeters | Strength at the motor mount
Supports | Minimal, by orientation | Less cleanup, better surface
Nozzle / bed | [__ °C] / [__ °C] | Per filament datasheet
These are typical starting values. Replace them with your own slicer profile.
Handheld 3D Printed Fan · Manufacturing Technology
10
Notes: Explain the trade-off behind each setting: more walls and infill add strength but also weight and print time. Print the blades with the surface facing up so layer lines do not run across the airflow, if your design allows.

## Slide 11: Bill of materials and assembly
04 · ASSEMBLY & COST
Item | Qty | Source | Cost (₹)
Filament for printed parts | 1 set | Printed | [__]
DC motor | 1 | Purchased | [__]
Li-ion cell and charger board | 1 | Purchased | [__]
Slide switch | 1 | Purchased | [__]
Wires, screws, solder | 1 lot | Purchased | [__]
Total |  |  | [__]
Assembly sequence
1 Fit the motor in its housing
2 Press the blade set onto the shaft
3 Wire the switch and cell
4 Close the handle and test
Handheld 3D Printed Fan · Manufacturing Technology
11
Notes: Fill in the cost column from your receipts and add the total. Mention that printed parts cost only the filament used, which is the main cost advantage of this approach.

## Slide 12: Hazards in making and using the fan
05 · ACCIDENT / HAZARD ANALYSIS
Hazard | Cause | Possible harm | Risk
Spinning blades | Finger enters the fan | Cuts, bruises | Medium
Li-ion cell | Short circuit, overcharge | Burns, fire | High
Hot nozzle and bed | Touched while printing | Burns | Medium
Print fumes | Heated filament, poor airflow | Irritation | Low
Blade fracture | Weak layers at high speed | Flying fragments | Medium
Sharp edges | Leftover supports | Small cuts | Low
Risk ratings are qualitative: severity of harm combined with how likely it is.
Handheld 3D Printed Fan · Manufacturing Technology
12
Notes: Cover the hazards from both stages: making the fan (hot printer, fumes) and using it (blades, battery). The ratings are a starting point; adjust them to your own judgement or to your department's risk matrix if one was taught.

## Slide 13: Safety devices and standards
06 · SAFETY DEVICES / STANDARDS
Built-in safety devices
Guard grill: gaps too small for a finger
Protection board: cuts off overcharge and short circuit
Slide switch: clear on and off control
Rounded edges: no sharp corners on handle or guard
Standards referred to
IEC 60335-2-80: safety of household fans
IEC 62133-2: safety of portable lithium cells
ISO/ASTM 52900: additive manufacturing terms
IS 302 (Part 1): household appliance safety, India
Used as design guidance. The prototype is not certified.
Handheld 3D Printed Fan · Manufacturing Technology
13
Notes: Link each safety device to a hazard on the previous slide: guard for blades, protection board for the cell. Be clear that the standards were used for guidance only; a certified product would need formal testing.

## Slide 14: Ergonomics and user comfort
07 · HUMAN FACTORS
Grip
Handle diameter of [__] mm suits a one-hand grip.
Weight
Light enough to hold for several minutes without tiring.
Noise and vibration
Balanced blades keep noise and hand vibration low.
Human error
Polarity-safe connectors and clear labels prevent wrong wiring and misuse.
Handheld 3D Printed Fan · Manufacturing Technology
14
Notes: Human factors covers both comfort and mistakes. Mention who will use the fan, including children, and how the design reduces the chance of misuse. Add your measured handle diameter.

## Slide 15: Preventing accidents at every stage
08 · PREVENTIVE MEASURES
In design
Guard gaps smaller than a finger
Rounded edges and fillets
Blade clearance and balance check
In printing
Print in a ventilated area
Keep hands off the hot nozzle and bed
Use the filament’s rated temperatures
In use
Charge only with the matching charger
Stop if the casing warms or cracks
Inspect blades for cracks before use
Handheld 3D Printed Fan · Manufacturing Technology
15
Notes: Match each measure to a hazard from the analysis slide. Design-stage measures are the strongest because they remove the hazard rather than relying on the user to behave carefully.

## Slide 16: How the prototype performed
09 · TESTING & RESULTS
[__] m/s
Air speed at 30 cm
[__] h
Run time per charge
[__] g
Total weight
[__] dB
Noise at 1 m
OBSERVATIONS
[Blade wobble, motor or casing heating, print defects, and the fixes you made.]
Handheld 3D Printed Fan · Manufacturing Technology
16
Notes: Replace the placeholders with your measured values. Say how you measured each one, for example an anemometer for air speed, a timer for run time, a kitchen scale for weight and a phone app for noise. Add photos of the finished fan if you can.

## Slide 17: Conclusion and future scope
10 · CONCLUSION
What we achieved
A handheld fan was designed in CAD and made mainly by FDM printing.
Material, print settings and assembly balanced weight, strength and cost.
Hazards were identified and reduced with a guard, battery protection and safe handling steps.
Future scope
Variable speed control
Blade profile tuned with airflow simulation
Foldable or modular housing
Recycled filament
Handheld 3D Printed Fan · Manufacturing Technology
17
Notes: Tie the conclusion back to the objectives on slide 2, one by one. Then give two or three future improvements. Keep this slide to about one minute.

## Slide 18: References
11 · REFERENCES
1 IEC 60335-2-80, Household and similar electrical appliances: safety requirements for fans.
2 IEC 62133-2, Safety requirements for portable sealed secondary lithium cells and batteries.
3 ISO/ASTM 52900, Additive manufacturing: general principles, fundamentals and vocabulary.
4 IS 302 (Part 1), Safety of household and similar electrical appliances: general requirements.
5 [Filament manufacturer datasheets for the material you used]
6 [Course textbook on additive manufacturing: author, title, year]
7 [Any papers, websites or CAD resources you used]
Handheld 3D Printed Fan · Manufacturing Technology
18
Notes: Check the exact edition or year of each standard against your library or department access before submitting, and fill in the bracketed entries with your own sources.

## Slide 19: Thank you
Questions and feedback
[Member names] · [Department, Institute]
Notes: Invite questions. Likely ones: why this filament, how the blades were balanced, and what the biggest safety risk was.